# 原子无序对half-Heusler合金CoCrAl电子结构及Seebeck系数的影响

### 论文摘要

采用真空电弧熔炼和放电等离子烧结技术制备了half-Heusler合金CoCrAl,利用XRD对合金的物相结构进行表征,借助相关设备测试了合金的饱和磁矩及Seebeck系数,并将实验结果与分别基于C1b有序、XY及YZ无序结构的CoCrAl合金的模拟计算值进行比较。结果表明,所制CoCrAl合金样品中除了完全有序的C1b结构相外还存在XY及YZ无序相。合金样品表现出典型的磁性金属特性且其Seebeck系数（绝对值）随着温度的升高呈先增加后降低的趋势,这与利用VASP和BoltzTraP软件包结合计算得到的CoCrAl合金的Seebeck系数随温度（300～800K）的变化趋势相符合。

### 论文目录

- 1 理论计算与实验方法

- 1.1 模拟与计算方法

- 1.2 实验方法

- 2 结果与讨论

- 2.1 模拟计算结果与讨论

- 2.2 实验结果与讨论

- 3 结语

### 文章来源

类型: 期刊论文

作者: 李春蓉,卢志红,王文静,尹航

关键词: 原子无序,合金,热电性能,电子结构,系数

来源: 武汉科技大学学报 2019年03期

年度: 2019

分类: 工程科技Ⅰ辑,工程科技Ⅱ辑

专业: 金属学及金属工艺,机械工业

单位: 武汉科技大学省部共建耐火材料与冶金国家重点实验室

基金: 国家自然科学基金资助项目(11574242)

分类号: TG146.16

页码: 182-186

总页数: 5

文件大小: 811K

下载量: 47

### 相关论文文献

- [1].The effects of interface scattering on thermoelectric properties of film thermoelectric materials[J]. Chinese Science Bulletin 2014(25)

- [2].Impact of grain size on the Seebeck coefficient of bulk polycrystalline thermoelectric materials[J]. Chinese Science Bulletin 2010(01)

- [3].Bipolar Thermoelectrical Transport of Sn Se Nanoplate in Low Temperature[J]. Chinese Physics Letters 2020(01)

- [4].Seebeck效应的教学体会[J]. 教育教学论坛 2017(14)

- [5].热电材料Seebeck系数测定中的误差分析[J]. 科技风 2014(17)

- [6].Optoelectronic properties and Seebeck coefficient in SnSe thin films[J]. Journal of Semiconductors 2016(09)

- [7].塞贝克系数的估算[J]. 科技创新与应用 2020(02)

- [8].基于Seebeck效应的配电变压器绕组材质无损鉴别装置及测试分析[J]. 电力自动化设备 2019(02)

- [9].碳纤维水泥基复合材料Seebeck效应研究现状[J]. 材料导报 2017(01)

- [10].Experimental studies on overall property of thermoelectric modules with sandwiched structures[J]. Chinese Science Bulletin 2014(Z1)

- [11].钢渣混凝土的Seebeck效应研究[J]. 重庆建筑大学学报 2008(03)

- [12].Thermoelectric properties of LaFe_3CoSb_(12) skutterudite materials with different nanostructures[J]. Journal of Rare Earths 2011(10)

- [13].First principle investigation of the electronic and thermoelectric properties of Mg_2C[J]. Chinese Physics B 2016(02)

- [14].Research on the Seebeck effect in efficient turning process and improving tool life[J]. Journal of Harbin Institute of Technology 2012(06)

- [15].Thermoelectric properties of Bi_(1.5)Pb_(0.5)Sr_(2-x)La_xCo_2O_y polycrystalline materials[J]. Rare Metals 2011(05)

- [16].HPHT synthesis and electrical transport properties of Sm_xCo_4Sb_(12)[J]. Journal of Rare Earths 2010(03)

- [17].Thermoelectric transport properties of Bi CuSeO with embedded La0.8Sr_(0.2)CoO_3 nanoinclusions[J]. Science China(Technological Sciences) 2016(07)

- [18].Synthesis and high temperature thermoelectric transport properties of Si-based type-Ⅰ clathrates[J]. Chinese Physics B 2009(07)

- [19].Transport properties of Zintl phase Yb_(1-x)Ca_xCd_2Sb_2 at low temperature[J]. Journal of Rare Earths 2010(03)

- [20].Preparation and Thermoelectric Properties of SiO_2/β-Zn_4Sb_3 Nanocomposite Materials[J]. Journal of Wuhan University of Technology(Materials Science Edition) 2009(05)

- [21].自旋Seebeck效应实验研究进展[J]. 材料导报 2015(05)

- [22].Electrical Properties of GeTe-based Ternary Alloys[J]. Journal of Wuhan University of Technology(Materials Science) 2018(02)

- [23].Recent Progress of Two-Dimensional Thermoelectric Materials[J]. Nano-Micro Letters 2020(03)

- [24].Graphene-enhanced thermoelectric properties of p-type skutterudites[J]. Chinese Physics B 2018(04)

- [25].Electronic structures and thermoelectric properties of solid solutions CuGa_(1-x) In_xTe_2 : A first-principles study[J]. Chinese Physics B 2014(03)

- [26].Anion-site-modulated thermoelectric properties in Ge_2Sb_2Te_5-based compounds[J]. Rare Metals 2020(10)

- [27].Preparation and electronic characteristics of anionic perylene bisimide films[J]. Science China(Chemistry) 2017(10)

- [28].Effect of pressure on electronic and thermoelectric properties of magnesium silicide: A density functional theory study[J]. Chinese Physics B 2016(05)

- [29].Effect of manganese doping on the thermoelectric properties of Zintl phase EuCd_2Sb_2[J]. Journal of Rare Earths 2015(10)

- [30].自旋Seebeck效应简介[J]. 物理 2011(11)

本文来源: https://www.lunwen90.cn/article/239f9878cda9497e262059da.html