# Volumetric changes in the focal areas of seismic events corresponding to destress blasting

### 论文摘要

The typical development of total volumetric change in the focal areas of seismic events, corresponding to destress blasting, is characterized as an explosive phase followed by an implosive phase and with alternating additional phases following on from that. In a few cases, a non-typical development of volumetric change was identified, where the first phase was implosive and the second phase, explosive. This development is mainly typical for induced seismic events recorded during mining, not for destress blasting.Seismic events were recorded during longwall mining in the Czech part of the Upper Silesian Coal Basin, where the destress blasting technique is used as a rockburst prevention active measure.Kinematic source processes in the focal areas of selected seismic events were analyzed by the seismic moment tensor inversion method, as well as by studying geomechanical rock mass conditions at the localities of the seismic events. The main goal of the analysis was to attempt to identify the reasons for non-typical development of volumetric changes in these cases. Volumetric changes were analyzed for seismic events with energy greater than 104 J, recorded in the period of time from 1993 to 2009（1109 events）. 80%（891） of the recorded seismic events were induced seismic events that were registered during longwall mining and 20%（218） corresponded to destress blasting events. Research shows that the main reason for the non-typical development of volumetric changes in the focal areas of seismic events is an association with destress blasting in the rock mass, which is very close to rock mass overstressing. The detonation of explosives in boreholes, which would dominate the first phase of volumetric changes, probably obscured stress release in the rock mass, as manifested in the first implosion phase of the volumetric changes in this case.

### 论文目录

- 1. Introduction

- 2. Seismological monitoring

- 3. Longwall No.1

- 4. Longwall No.2

- 5. Conclusions

### 文章来源

类型: 期刊论文

作者: P.Konicek,J.Schreiber,L.Nazarova

来源: International Journal of Mining Science and Technology 2019年04期

年度: 2019

分类: 工程科技Ⅰ辑

专业: 矿业工程

单位: Department of Geomechanics and Mining Research, Institute of Geonics of the Czech Academy of Sciences,Laboratory of Mining Informatics, Chinakal Institute of Mining of the Siberian Branch of the Russian Academy of Science

基金: the project of the Institute of Clean Technologies for Mining and Utilisation of Raw Materials for Energy Use–Sustainability Programme(No.LO1406),supported by a project for the long-term conceptual development of research organisations(No.RVO68145535)

分类号: TD326

页码: 541-547

总页数: 7

文件大小: 4753K

下载量: 3

### 相关论文文献

- [1].Evaluation and optimization of blasting approaches to reducing oversize boulders and toes in open-pit mine[J]. International Journal of Mining Science and Technology 2020(03)

- [2].Understanding the connection between blasting and highwall stability[J]. International Journal of Mining Science and Technology 2019(01)

- [3].Evaluation of human response to blasting vibration from excavation of a large scale rock slope:A case study[J]. Earthquake Engineering and Engineering Vibration 2017(02)

- [4].Effects of torpedo blasting on rockburst prevention during deep coal seam mining in the Upper Silesian Coal Basin[J]. Journal of Rock Mechanics and Geotechnical Engineering 2017(04)

- [5].Rock-breaking mechanism and experimental analysis of confined blasting of borehole surrounding rock[J]. International Journal of Mining Science and Technology 2017(05)

- [6].Analysis of key technologies and development of integrated digital processing system for cast blasting design[J]. Journal of Central South University 2015(03)

- [7].Analysis of blasting damage in adjacent mining excavations[J]. Journal of Rock Mechanics and Geotechnical Engineering 2015(03)

- [8].Modified scaled distance regression analysis approach for prediction of blast-induced ground vibration in multi-hole blasting[J]. Journal of Rock Mechanics and Geotechnical Engineering 2019(01)

- [9].Kinetic energy and its applications in mining engineering[J]. International Journal of Mining Science and Technology 2017(02)

- [10].Developing a mathematical assessment model for blasting patterns management: Sungun copper mine[J]. Journal of Central South University 2014(11)

- [11].Research on the inwall shot blasting of the S30432 high-pressure boiler tube[J]. Baosteel Technical Research 2012(01)

- [12].Optimization and application of blasting parameters based on the "pushing-wall" mechanism[J]. International Journal of Minerals Metallurgy and Materials 2012(10)

- [13].Time-frequency characteristics of blasting vibration signals measured in milliseconds[J]. Mining Science and Technology 2011(03)

- [14].Analysis on control technology for collapsing vibration generated by building demolition blasting[J]. Journal of Coal Science & Engineering(China) 2010(03)

- [15].Numerical simulation of stress for the blasting of foundation pit[J]. Journal of Coal Science & Engineering(China) 2008(04)

- [16].Analysis of the blasting effect on the electric shove loading efficiency of the open pit[J]. Journal of Coal Science & Engineering(China) 2008(04)

- [17].Field experiment for blasting crater[J]. Journal of China University of Mining & Technology 2008(02)

- [18].Numerical simulation of parallel hole cut blasting with uncharged holes[J]. Journal of University of Science and Technology Beijing 2008(03)

- [19].Prediction of flyrock in open pit blasting operation using machine learning method[J]. International Journal of Mining Science and Technology 2013(03)

- [20].Roof pre-blasting to prevent support crushing and water inrush accidents[J]. International Journal of Mining Science and Technology 2012(03)

- [21].Recrystallization of Ni_3 Al Base Single Crystal Alloy IC6SX with Different Surface Mechanical Processes[J]. Journal of Materials Science & Technology 2010(10)

- [22].Experimental study on stemming effect in rock blasting[J]. Engineering Sciences 2010(04)

- [23].Effectiveness analysis of methane-drainage by deep-hole controlled pre-splitting blasting for preventing coal and gas outburst[J]. Journal of Coal Science & Engineering(China) 2009(02)

- [24].Influence of millisecond time,charge length and detonation velocity on blasting vibration[J]. Journal of Central South University 2015(12)

- [25].A comparison of seismic response to conventional and face destress blasting during deep tunnel development[J]. Journal of Rock Mechanics and Geotechnical Engineering 2019(05)

- [26].Application of deep borehole blasting on fully mechanized hard top-coal pre-splitting and gas extraction in the special thick seam[J]. International Journal of Mining Science and Technology 2015(05)

- [27].Numerical study on the fracturing mechanism of shock wave interactions between two adjacent blast holes in deep rock blasting[J]. Earthquake Engineering and Engineering Vibration 2019(04)

- [28].Seismic effort of blasting wave transmitted in coal-rock mass associated with mining operation[J]. Journal of Central South University 2012(09)

- [29].Bond interface crack propagation of fresh foundation concrete and rock under blasting load[J]. Journal of Coal Science & Engineering(China) 2009(01)

- [30].Application of the L-M optimized algorithm to predicting blast vibration parameters[J]. Acta Seismologica Sinica(English Edition) 2008(05)

本文来源: https://www.lunwen90.cn/article/dab9e79bbeae9316f84962af.html