# Hot Deformation and Corrosion Resistance of High-Strength Low-Alloy Steel

### 论文摘要

The hot deformation characteristics and the corrosion behavior of a high-strength low-alloy（HSLA） steel were investigated at deformation temperatures ranging from 800 to 1100 ℃ and strain rates ranging from 0.1 to 10 s-1 using an MMS-200 thermal simulation testing machine. Based on the flow curves from the experiment, the effects of temperature and strain rate on the dynamic recrystallization behavior were analyzed. The flow stress decreased with increasing deformation temperature and decreasing strain rate. With the assistance of the process parameters, constitutive equations were used to obtain the activation energy and hot working equation. The hot deformation activation energy of HSLA steel in this work was 351.87 kJ/mol. The work hardening rate was used to determine the critical stress（strain） or the peak stress（strain）. The dependence of these characteristic values on the Zener-Hollomon parameter was found. A dynamic recrystallization kinetics model of the tested HSLA steel was constructed, and the validity of the model was confirmed by the experimental results. Observation of the microstructures indicated that the grain size increased with increasing deformation temperature,which led to a lowered corrosion resistance of the specimens.

### 论文目录

### 文章来源

类型: 期刊论文

作者: Wilasinee Kingkam,Cheng-Zhi Zhao,Hong Li,He-Xin Zhang,Zhi-Ming Li

来源: Acta Metallurgica Sinica(English Letters) 2019年04期

年度: 2019

分类: 工程科技Ⅰ辑

专业: 金属学及金属工艺

单位: College of Materials Science and Chemical Engineering,Harbin Engineering University,Key Laboratory of Superlight Materials and Surface Technology,Ministry of Education,Harbin Engineering University,College of Power and Energy Engineering,Harbin Engineering University

基金: supported financially by the Fundamental Research Funds for the Central Universities (Nos. HEUCFP201719 and HEUCFP201731)

分类号: TG142.33;TG156

页码: 495-505

总页数: 11

文件大小: 1174K

下载量: 14

### 相关论文文献

- [1].Study on degradation kinetics of epalrestat in aqueous solutions and characterization of its major degradation products under stress degradation conditions by UHPLC-PDA-MS/MS[J]. Journal of Pharmaceutical Analysis 2019(06)

- [2].Characteristics of micro-interface adsorption kinetics between sediments and Cu ions[J]. International Journal of Sediment Research 2017(01)

- [3].Comparison of desulfurization kinetics of copper oxide sorbent[J]. Journal of Central South University 2015(08)

- [4].A New Kinetic Mode During the Austenite-to-Ferrite Transformation in Fe–Mn and Fe–Mn–Mo Alloys[J]. Acta Metallurgica Sinica(English Letters) 2020(07)

- [5].Modulating charge separation and transfer kinetics in carbon nanodots for photoredox catalysis[J]. Journal of Energy Chemistry 2020(11)

- [6].Modelling of dynamic recrystallization kinetics of 300M steel at high strain rates during hot deformation[J]. Science China(Technological Sciences) 2019(09)

- [7].Study on the volatilization kinetics of zinc in carbon-containing pellets made of Zn-bearing dusts[J]. Baosteel Technical Research 2013(03)

- [8].Modeling of metadynamic recrystallization kinetics after hot deformation of low-alloy steel Q345B[J]. Journal of Central South University of Technology 2010(05)

- [9].Interfacial Reactive Kinetics of Back-Extraction of Pu(Ⅳ) From 30%TBP-OK With N,N-dimethylhydroxylamine[J]. Annual Report of China Institute of Atomic Energy 2008(00)

- [10].Brilliant red X-3B uptake by a novel polycyclodextrin-modified magnetic cationic hydrogel:Performance,kinetics and mechanism[J]. Journal of Environmental Sciences 2020(03)

- [11].Identification and interspecies characterization of UDP-glucuronosyltransferase isoforms catalyzing acacetin glucuronidation using recombinant UGT enzymes and microsomes[J]. Journal of Traditional Chinese Medical Sciences 2019(02)

- [12].Modeling of degradation kinetics of Salvianolic acid B at different temperatures and pH values[J]. Chinese Journal of Chemical Engineering 2017(01)

- [13].Dynamic recrystallization behavior and kinetics of high strength steel[J]. Journal of Central South University 2016(05)

- [14].CFD modeling using heterogeneous reaction kinetics for catalytic dehydrogenation syngas reactions in a fixed-bed reactor[J]. Particuology 2013(06)

- [15].Temperature effect on the kinetics of persulfate oxidation of p-chloroaniline[J]. Chinese Chemical Letters 2011(03)

- [16].Mechanism and kinetics of 2-chlorophenol decomposition using coupled ultrasound and electrocatalysis[J]. Science in China(Series B:Chemistry) 2008(06)

- [17].Study on kinetics of thermal decomposition of low LOI goethetic hematite iron ore[J]. International Journal of Mining Science and Technology 2017(06)

- [18].Technology and kinetics of free fatty acids esterification in tung oil[J]. Journal of Chongqing University(English Edition) 2009(02)

- [19].Study of adsorption kinetics for fluorescent whitening agent on fiber surfaces[J]. Science in China(Series B:Chemistry) 2008(05)

- [20].Numerical modeling of SiC by low-pressure chemical vapor deposition from methyltrichlorosilane[J]. Chinese Journal of Chemical Engineering 2020(06)

- [21].Preparation of supported nano-copper oxide and its sulfation kinetics[J]. Transactions of Nonferrous Metals Society of China 2009(S3)

- [22].Application of kinetics and computational fluid dynamics in pinene isomerization[J]. Chinese Journal of Chemical Engineering 2020(08)

- [23].Relationship between metabolic enzyme activities and bioaccumulation kinetics of PAHs in zebrafish(Danio rerio)[J]. Journal of Environmental Sciences 2018(03)

- [24].New bainite kinetics of high strength low alloy steel in fast cooling process[J]. Journal of Iron and Steel Research(International) 2017(02)

- [25].Study on the volatilization kinetics of lead in carbon- containing pellets made of Zn- Pb- bearing dusts[J]. Baosteel Technical Research 2014(04)

- [26].Thermodynamics and kinetics of extracting zinc from zinc oxide ore by the ammonium sulfate roasting method[J]. International Journal of Minerals Metallurgy and Materials 2015(05)

- [27].Efects of thermal aging temperature and Cr content on phase separ-ation kinetics in Fe-Cr alloys simulated by the phase feld method[J]. International Journal of Minerals Metallurgy and Materials 2013(11)

- [28].Synthesis, characterization of monodispersed MgO microspheres and thermal decomposition kinetics of its precusor[J]. Journal of Central South University 2014(09)

- [29].Dealumination kinetics of composite ZSM-5/mordenite zeolite during steam treatment: An in-situ DRIFTS study[J]. Chinese Journal of Chemical Engineering 2018(03)

- [30].Crystallization kinetics of Sn_(40)Se_(60) thin films for phase change memory applications[J]. Journal of Semiconductors 2015(06)

本文来源: https://www.lunwen90.cn/article/eae0d9b03891836c2f4d66c7.html